## Slide 1
TEAM
Meet the team
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
01 / 09
TEAM NAME
Tech Minions
MEMBER 1
Bhawna Singh
ROLE
Perception & ML
MEMBER 2
Aditya Singh
ROLE
Hardware & embedded
MEMBER 3
Harshit Vats
ROLE
Navigation & control
Problem Statement 01 · Vision-Based Autonomous Robot

## Slide 2
PROBLEM STATEMENT & THEME
Vision-Based Autonomous Robot
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
02 / 09
THE PROBLEM
How can a robot autonomously navigate unfamiliar campuses, hospitals, and warehouses—without a pre-built map?
Cluttered, changing scenes defeat fixed rules
Perception-to-action in ~0.2 s
Goals arrive as words, not coordinates
IMPACT
Logistics
Fetch-and-carry without fixed tracks or QR markers
Healthcare
Safe delivery around patients and staff
Assistive
Finds objects for visually impaired users
THEME ALIGNMENT
All 9 suggested technical directions are covered
Object detection
YOLO finds people, chairs, bottles and more
Image classification
Labels each detected object where needed
Scene understanding
Objects + sensor readings give the full picture
Vision-language model
Optional layer for “Go to the chair” commands
Motor control
Arduino Mega drives the four mecanum motors
Sensors & perception
Ultrasonic, LiDAR + camera see the surroundings
Autonomous navigation
Robot picks its own path toward the target
Obstacle avoidance
Spots nearby obstacles and changes direction
Real-time decisions
Sense → decide → move → check, in a loop

## Slide 3
THE SOLUTION
Say what to find. The robot goes there.
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
03 / 09
WHAT THE ROBOT SEES
LIVE CAM-0 10 FPS
person 0.94
TARGET chair 0.88
obstacle 0.6 m
Illustration of the live dashboard: target found, obstacle ahead, robot steers around it.
SOLUTION OVERVIEW
Say what to find, for example “go to the chair”. The robot sees it, picks its own path and drives there, sliding around obstacles and stopping for anything in the way.
KEY FEATURES
Voice-guided
Say the target and the robot finds and reaches it, no remote control needed.
Moves in any direction
Mecanum wheels slide sideways and spin in place, so it manoeuvres easily in narrow spaces.
Stable omnidirectional base
Aluminium chassis with the sensors built in, designed in Fusion 360.
Safe by design
Stops if something is under 25 cm, the link drops or STOP is touched.
UNIQUE VALUE
A low-cost robot that understands spoken goals, yet keeps its safety reflexes on the robot, so it stays safe even when the AI lags.

## Slide 4
ARCHITECTURE 1 / 2 ARCHITECTURE 2 / 2
Hardware & circuit Software & data flow
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
04 / 09
Laptop · Python
Vision
OpenCV · Ultralytics · ESP32-CAM stream
Voice
SpeechRecognition + Vosk / Whisper
Mapping & planning
BreezySLAM · NumPy · A* + DWA
Comms & UI
websockets · asyncio · Streamlit
Robot firmware · C++
ESP32 (Arduino core)
WebSocket · LiDAR (UART2) · relay
Arduino Mega 2560
Mecanum IK · PID · 50 Hz · watchdog
Sensor libraries
NewPing · MPU6050 · Encoder
Status display
Adafruit GFX: target, decision, battery
01
Command
Voice or text goal from the laptop mic
02
Perceive
YOLO11n detects and tracks objects in each frame
03
Map
LiDAR + ultrasonic + IMU + encoders build an occupancy grid
04
Decide
State machine + A* / DWA pick heading and speed
05
Send
JSON over WebSocket to ESP32, UART to Mega
06
Drive
Mecanum IK + PID turn velocity into PWM
Notes: Laptop does the heavy AI and talks to the ESP32 over Wi-Fi. ESP32 also reads the LiDAR. The Mega runs the motors through four BTS7960 drivers and reads the ultrasonic sensors, IMU and attachment ID. One 4S pack feeds a 14.8 V rail plus 5 V and 6 V bucks.

## Slide 5
DECISION MAKING
How it decides
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
05 / 09
1. Understand the goal
USER SAYS
"Go to the person near the red chair"
Vision-language model + camera frame + YOLO detections
{ "target": "person", "track_id": 7,
"anchor": "red chair", "conf": 0.86 }
The VLM runs about once a second; YOLO keeps tracking the target at 10 FPS in between.
Safety reflex · always wins
Ultrasonic or LiDAR under 25 cm, or no command for 0.5 s → stop, whatever the planner says.
2. Act on it: state machine
SEARCH
APPROACH
ARRIVED
AVOID
target found
lost > 2 s
dist < 0.5 m
obstacle < 40 cm
path clear
Every cycle: read sensors → update tracks → check transitions → send velocity. Budget under 100 ms.
Notes: The language model turns a sentence into a concrete target; the state machine then searches, approaches, avoids and stops. The safety reflex overrides everything.

## Slide 6
MARKET
A fast-growing market
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
06 / 09
$16.9B
Global autonomous mobile robot market by 2033
15–18%
Annual growth (CAGR) 2025–2033 across analyst estimates
$2.8–5.1B
Market size estimates for 2024–25
Target users
Warehouses & logistics SMEs
Hospitals and care homes
Campuses, malls, security teams
Assistive-tech providers
Revenue model
Robot kit + software licence
Robot-as-a-Service subscription
Licensing the perception stack
Custom integration & support
Expected growth
Year 1: campus pilot, 2–3 robots
Year 2: logistics SME pilots
Year 3: fleet product + RaaS
Rides 15%+ yearly AMR growth
Sources: IMARC Group, Autonomous Mobile Robots Market 2025–2033; Global Market Insights, AMR Market 2025–2034.
Notes: AMR market roughly 17 billion dollars by 2033 at 15-18% a year. Users, revenue model and a three-year growth plan.

## Slide 7
FUTURE SCOPE
Where we go next
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
07 / 09
01
Mobile app deployment
Remote monitoring, task assignment, robot status and basic control through a dedicated mobile app.
Monitor
Assign tasks
Basic control
02
Enterprise integrations
Connect with hospitals and industrial systems for workflows, scheduling, alerts and operational data.
Workflows
Scheduling
Alerts
03
AI model improvement
Stronger VLM and vision models for better scene understanding, target recognition and decision making.
Stronger VLM
Vision models
Decisions
04
Scaling to global users
Expand across multiple sites, environments and use cases with scalable deployment and software updates.
Multi-site
New use cases
Updates

## Slide 8
HACK IN HILLS · VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS
08 / 08
Thank you
Questions?
VISION-BASED AUTONOMOUS ROBOT · TECH MINIONS